Monte Carlo Dynamic Event Tree     +        MELCOR

An Example of a Stochastic Module*) coupled
with an Integral Code#) for PSA Level 2

Martin Sonnenkalb#)
GRS Cologne, Germany

Joerg Peschke, Martina Kloos, Bernard Krzykacz*)
GRS Munich, Germany

Content of Presentation

Examples of MELCOR Application for German LWR

Probabilistic Dynamics

What does it mean - Probabilistic Dynamics?

Kinds of Uncertainty within the framework of PSA

Limitations of Event Trees in current PSA Level 2

Other Methods of Probabilistic Dynamics

Example of a Dynamic Event Tree

Basics of New Method MCDET

Dynamic Event Tree with MCDET (and with MELCOR)

Realised Steps in a Prototype Application

Assumptions/Events of SBO-Sequence

First Results and Summary

Examples of MELCOR Application for German LWR

What does it mean - Probabilistic Dynamics?

Probabilistic dynamics is concerned with dynamics (evolution of the physical variables e.g. during a severe accident) and their interaction with the random evolution of parameters (e.g. component behaviour or NPP operator states). Smidts (1994)

Dynamic reliability methods provide a framework for explicitly capturing the influence of time and process dynamics on scenarios. Labeau, Smidts, Swaminathan (2000)

The evolution of an accident is time dependent and determined by the interaction of dynamics and stochastic in a system consisting of man, machine, process and environment. Accidents to be considered in PSA level 2 analysis comprise time dependent events (sequence of -, duration of - and time difference between actions) as well as interactions between process-dynamic and stochastic elements.  Hofer (2000)

Kinds of Uncertainty within the framework of PSA

Aleatoric Uncertainty                                                     NRC (1998), Parry (1996)
The aleatoric uncertainty is that addressed when the events or phenomena being modelled are characterised as occurring in a “random” or “stochastic” manner, and probabilistic models are adopted to describe their occurrence. It is this aspect of uncertainty that gives PRA the probabilistic part of its name.

Epistemic Uncertainty                                          NRC (1998), Parry (1996)
The epistemic uncertainty is that associated with the analyst’s confidence in the predictions of the PRA model itself, and it reflects the analyst’s assessment of how well the PRA model represents the actual system being modelled. This has been referred to as state-of-knowledge uncertainty.

The customary uncertainty analysis determines the influence of knowledge uncertainties (epistemic uncertainties) in parameters, model formulations, phenomena as well as in numerical solution algorithms on the results of computer model applications (e.g. ATHLET, MELCOR). Analyses of this kind have been performed with the GRS code SUSA since many years. Glaeser(1995), Hofer (1996)

The aleatoric uncertainties are taken into account in the new method MCDET.

Limitations of Event Trees in current PSA Level 2

Characterisation of numerous possible accident scenarios only by:

coarse assessment scheme related to:

“time”, e.g. of an event - early, late, before or after something happens

“position”, e.g. of a break - high, low

“intensity”, e.g. of a combustion - strong, negligible

... etc.

simplification of interactions between phenomena, processes, human action

Risk to:

not consider some contexts of events or scenarios,

not detect events or scenarios which would result from detailed simulation of phenomena, processes, human action, etc.

generate unrealistic events or scenarios due to bad analyst defined conditions

Basics of the new method Monte Carlo Dynamic Event Tree                (1)

MCDET:

use of a stochastic module connected with a dynamic code – MELCOR used in the example

Features of the Stochastic Module:

modelling of stochastic influences – shake hands with the dynamic code

determination of probability distributions of different dynamic code results like:

occurrence of a failure dependent e.g. on the kind of the failure and its timing

value or time dependent value of a dynamic process variable

a vector of dynamic process variables (release rate of different fission products)

determination of importance of measures

identification of each calculated accident sequence

simplified customary uncertainty and sensitivity analysis

Basics of the new method Monte Carlo Dynamic Event Tree                   (2)

Application of MCDET to MELCOR

preparation of an interface program between MCDET and MELCOR:

- to generate MELCOR input

- to read the MELCOR  message file with information needed in MCDET

- to automatically start and stop all sequences

manipulation of system availabilities by Control Functions in MELCOR

calculation of base sequence first, other sequences continuing from Restart

messagef         '/temp/pej/message/m#*-99'

edf00101         '/temp/pej/out/r#*-98'

exacttime1    #*002

restartcf        438  * Restart at SG-Signal o. Valve ...

restart   time  #*001

tend               #*002

* Pres. Valve PORV, SRV1 + SRV2

cf42100  'porv logic'   l-a-ifte  3        #*003      #*004

cf42101  0.0

cf43100  'srv1 logic'   l-a-ifte  3        #*005      #*006

cf43101  0.0

cf44100  'srv2 logic'        l-a-ifte  3        #*007      #*008

cf44101  0.0

* HP-Pump 1 HL

cf04100  '1x HP-SiP'       tab-fun  1       #*009      #*010

cf04101  0.0

* HP-Pump 2 HL

cf04200  '1x HP-SiP 3A'  tab-fun  1       #*011      #*012

cf04201  0.0

Other Methods of Probabilistic Dynamics

explicit methods

requiring, that the analyst explicitly defines all system states and its transitions

(  well known as “ Markov-Models”

implicit methods

implicit definition of the system states and its transitions dependent on the rules provided by the analyst

( known as “Dynamic Event Trees”

( methods or codes described in the literature are e.g.:
     DYLAM [Cojazzi (1996)], DETAM [Siu (1994)], ADS [Chang (1998)], ISA [Asensio [1997)]

Example of a Dynamic Event Tree

# Dynamic Event Trees consider the influence of time in detail not only be characteristic states

Dynamic Event Tree with MCDET (and with MELCOR)

#  Dynamic Event Trees consider the influence of time and the interaction between dynamic and stochastic events

#  1 of N Dynamic Event Trees with different types of branch points according to MCDET

Realised Steps in a Prototype Application                           (1)

Realised Steps in a Prototype Application                           (2)

Identification of stochastic elements, e.g.:

Active Components (AC)

pressuriser relief and safety valves

pumps and valves of HP and LP safety injection systems

valves in accumulator system

Passive Components (PC)

reactor pressure vessel

hot leg, pressuriser surge line

containment

Human Action (HA)

determination of plant status

activation of systems

AM measure: primary bleed

Phenomena (PH) not modelled e.g. in MELCOR

a molten pool inside reactor core, (coolability, recriticality)

hydrogen detonation

steam explosion

External (EX) stochastic events

recovery of external power supply

switch back of each of the 4 different ECC trains

status of systems at time of power recovery

Realised Steps in a Prototype Application                           (3)

Identification of stochastic variables, e.g.:

AC – function of pressuriser relief valve:

normal operation

failure to open

failure to close (stuck open)

manual depressurisation OK

failure to open during manual
operation

PC – failure criteria for RPV and reactor circuit components

HA – time needed to perform AM measure “primary bleed”

EX – time difference between initial event and power recovery

Identification of time and system states where a stochastic impact will occur

Identification of time-state-windows (combinations of time and system states) for different distributions of stochastic variables – failure function of valves

How many times the pressurizer relief valve has opened/closed already during pressure limitation process at ~16 MPa?

Realised Steps in a Prototype Application                           (4)

Specification of probability distributions for each stochastic variable of the time-state-window - defined

Do we need additional physical models?

PH – to simulate coolability of a molten pool inside the core region? – yes, but not done in example

PH – to simulate re-criticality? – no

Implementation of needed physical models – no model in this application

Determination of additional stochastic variables in added models – no variables

Determination of  conditions indicating where the dynamic calculation should end

successful core cooling or RPV failure or process time greater 12000 sec

Assumptions/Events of SBO-Sequence                               (1)

MELCOR Input Deck Requirements

practically no limitations

all states of systems (AC, PC) modelled by Control Function

Control Function values are modified during Restart

modifications are generated automatically by one of the MCDET modules

main interesting parameter written by External Data File (predefined !!)

Assumptions/Events of SBO-Sequence                            (2)

Timing of Events:

SBO, MCP off, RESA: 0 s - 3 s

SG empty: ~3600 s

1st opening of press. RV ~4000 s

1st release into containm. ~5300 s

AM measure - Bleed: ~6220 s

begin of FP gap release w/o
reflooding : ~8400 s

begin of core melting w/o
reflooding : ~9000 s

threshold for path-probability:         < 1. E-04

Stochastic Events – First Event-Tree out of N with randomly defined values

different failure modes of press. valves after M cycles of operation
48 - RV, 43 - SV1, 4 - SV2

only “available” valves can be opened by AM measure “Bleed”

time needed to initiate AM measure after process signal: 325 s

different states of “available” valves after AM measure “Bleed”

different states of accumulators

different time until recovery of power in each of the 4 different ECC trains: 7038 s, 7488 s, 7938 s, 8388 s

different states of valves and safety injection pumps in each ECC train after power recovery

failure criteria for MCL and surge line (not relevant in this set)

Containment Pressure – Results of all sequences calculated with 1 of N sets of stochastic data

RPV Pressure – Results of all sequences calculated with the 1st set of stochastic data out of N

Total H2 mass – Results of all sequences calculated with the 7st set of stochastic data out of N

RPV Water Level – Results of all sequen. calculated with the 1st set of stochastic data out of N

Probability Distribution - Minimum of RPV Water Level
Results of all sequences calculated with the 1st set of stochastic data out of N

Probability Distribution - Maximum of Core Exit Temperature
Results of all sequences calculated with the 1st set of stochastic data out of N

Summary

MCDET allows:

to be added as module to different dynamic codes (MELCOR, ATHLET, ...)

a consideration of a wide spectrum of stochastic influences (AC, PC, HA, PH, EX)

to use multiple branching points

consideration of continuous stochastic transitions by Monte Carlo method

different dependencies of stochastic elements (time, status, history of accident)

status change of multiple number of stochastic elements within one time step

uncertainty and sensitivity analysis (simplified)

use of parallel processor units for speed up

CPU time required for calculations with first set of stochast. data

~150 sequences calculated with 1st set of stochastic data

only a very few abnormal ends of MELCOR runs

~ 3 - 5 d needed on a DEC-ALPHA Workstation here without parallel jobs

more information in next paper of Löffler/Peschke GRS

# Text boxes

The MCDET stochastic module is developed at 
Gesellschaft für Anlagen- und Reaktorsicherheit (GRS) mbH

Project - MCDET and MELCOR since 2000

PWR

Test of new Features

10/1994:  MELCOR 1.8.3

9/1997:  MELCOR 1.8.4

Severe Accident Analysis

for PSA Level 2 Analysis

11/2000:  MELCOR 1.8.5

Severe Accident Training Course by ATLAS
Simulator

Severe Acci-            dent Analysis      for Plant Specific PSA Level 2 BWR type 69

Severe Accident Analysis

replacing STCP

Preparation of PSA

Severe Accident Training Course by ATLAS
Simulator

Severe Accident Analysis

for Generic PSA Level 2 Analysis

Severe Accident Analysis

Investigation of AM measures (e.g. hydrogen issue)

Input Deck development and code-to-code comparison

1992:  MELCOR 1.8.2

Input Deck development and validation

BWR

fts – failure to start 
(a valve fails to open at request);

ftr – failure to run 
(a valve fails after x cycles);

threshold – branch not considered further due to low probability

.

.

.

N

fts – failure to start;

ftr – failure to run;

threshold – branch not considered due to low probability

det – deterministic

prob – probabilistic

MC – Monte Carlo

PH - Phenomena

Specification of Initial Conditions, e.g.:

PWR-1300 at nominal power

initial event: total station black out

Identification of important process variables
and system states, e.g.:

core exit temperature

core or RPV water level

degree of core degradation (amount of melt, hydrogen, ...)

probability distributions of process parameters dependent on time, location, etc.

Determination of dynamic code, e.g.:

MELCOR with PWR-1300 input deck

cumulative probability

cumulative probability