Assembly Type 4

Schematic of the Ferrule Spacer

Estimates of the Ferrule Spacer Dimensions

Assumptions:

- Thickness of 0.5 mm;

- Homogeneous arrangement.

Dimensions used as reference values:

- Outside rod diameter of 12.3 mm;

- Outside water rod diameter of 34.0 mm;

- Rod pitch of 16.2 mm;

- Ferrule spacer total width of 132 mm.

Technique used:

- Simple measuring/scaling technique by applying two different scale ratios (vertical and horizontal) to the side view drawings (as provided by JNES).

- Adjustments to the above-mentioned reference values to match all dimensions.

Comment:

Errors are possible because the graphics made available might have been deformed through different copying processes.

Ferrule Spacer Dimensions

Top view – corner of the bundle

Top view – center of the bundle

Side view

# Text boxes

7.4

4.7

3.3

132.0

0.7

22.0

15.0

3.6

3.8

45°

3.3

3.6

31.0

4.6

0.5

4.6

3.7

34.0

10.2

2.6

15.2

2.9

0.5

4.7

3.3

1.0

3.3

0.5

16.2

0.5

0.7

11.2

1.6

15.5

0.5

1.933

2.88

3.2

1.6

15.5

0.5

1.933

2.88

3.2